I working with openwrt or bitbake to build linux images for embedded devices.
These systems are robust and affidable but too complicate to debug.
With this project I have try to develop a simple method to generate a linux image with the only aid of script bash.
The result is only one shell bash script …

A.C.
Chapter I

RECIPES

Recipes are list of instruction and commands to inform the build system how make a project , as in bitbake.
In EGG the recipes are written with support of xml format . To parse the xml files in the bash script I use the xmlstarlet utility.

In general the structure of one recipes is like the following schema . Ex:

<?xml version="1.0"?>
<egg>
  <project>
    <name>busybox</name>
    <remote>
…..
    </remote>
    <build>
      <step id="0”>
…..
</step>
      <step id="1”>
…..
</step>
    </build>
  </project>
</egg>

As in xmlstarlet to refer a xml node , ex <egg><project><name> use the syntax egg/project/name.
Into node remote and step NN there are many nodes in function of the project request.

Every recipes must be saved in a file named conf.egg and store into a folder with the same name of the field egg/project/name. So a complete build system must be a collection of folders into a single main forlder. This main folder I named ‘repo’ from repository. Ad example the folder rpi2_repo have the following tree files
.
├── busybox
│   ├── busybox_defconfig_arm
│   ├── busybox_init
│   └── conf.egg
├── conf.egg
├── linux
│   └── conf.egg
└── uboot
    └── conf.egg

the conf.egg file on main folder rpi2_repo is a special file : it describe the configuration file for all recipes into repo. Ad ex for this repo the file contain:

<?xml version="1.0"?>
<egg>
  <conf>
-----
  </conf>
  <defaults>
    <step id="0">
      ….
    </step>
    <step id="1">
      ...
    </step>
  </defaults>
</egg>

Both the recipes as the main configuration is organizzed by step or level so a same recipes can build a different out because at every step can configure compile, option , architetture. In this mode is very fast the reuse of the recipes.

Recipes description:

Name
FIELD	OPT	DESCRIPTION
egg/project/name	no	Insert the project name .Must be the name of the folder where is the file conf.egg

Remote
FIELD	OPT	DESCRIPTION
egg/project/remote/method	no	Available method: wget,git,svn,apt,file(rsync)
egg/project/remote/url	no	Url to file to download , (with no filename...)
egg/project/remote/file	no	Url to file to download , (only filename )
egg/project/remote/key/url	yes	Url to sign file to download , (with no filename…)
egg/project/remote/key/file	yes	Url to file to download , (only filename )
egg/project/remote/branch	yes	In case of git method can insert branch to download
egg/project/remote/revision	yes	In case of svn method can insert revison to download

Example of remote node :

    <name>linux</name>
    <remote>
      <method>git</method>
      <url>https://github.com/raspberrypi</url>
      <file>linux.git </file>
      <branch>rpi-4.12.y</branch>
    </remote>

Build
FIELD	OPT	DESCRIPTION
egg/project/build/step id=N	no	Define the step N of build
egg/project/build/silent	no	Can define verbose build with ‘no’ or mute build ‘yes’
egg/project/build/thread	no	Define max thread num to make (-jN)
egg/project/build/path	yes	Define an action to current $PATH variable. In this can define action before the build action and after the build action. / Insert pre node to add an action before the build action for this step and insert the post node to add an action after the build action .
egg/project/build/path/pre	yes	Change the $PATH before build action
egg/project/build/path/post	yes	Change the $PATH after build action
egg/project/build/path/pre/set	yes	Set the $PATH in function of the value inserted in this node before the build step
egg/project/build/path/pre/add id = N	yes	Add to current $PATH the value inserted in this node, can insert more node in sequence order with the id field
egg/project/build/path/pre/remove id = N	yes	Remove from the current $PATH the value inserted in this node, can insert more node in sequence order with the id field
egg/project/build/path/post/set		Set the $PATH in function of the value inserted in this node after the build step
egg/project/build/path/post/add id = N		Add to current $PATH the value inserted in this node, can insert more node in sequence order with the id field
egg/project/build/path/post/remove id = N		Remove from the current $PATH the value inserted in this node, can insert more node in sequence order with the id field

Example path pre/post

<path>
        <pre>
        <set >$USER_PATH</set> bash shell accept any current defined shell variable
        </pre>
</path>

egg/project/build/configure	yes	Define the configure step : can be optional if configure , configure.ac or Makefile.ac isn’t defined in source files.
egg/project/build/configure/pre