RECIPES

Recipes are list of instruction and commands to inform the build system how make a project , as for example in bitbake.
In EGG the recipes are written with support of xml format . To parse the xml files in the bash script I use the xmlstarlet utility.

In general the structure of one recipes is like the following schema . Ex:

<?xml version="1.0"?>
<egg>
  <project>
    <name>busybox</name>
    <remote>
…..
    </remote>
    <patch>
…..
    </patch>
    <build>
      <step id="0”>
…..
</step>
      <step id="1”>
…..
</step>
    </build>
  </project>
</egg>

As in xmlstarlet to refer a xml node , ex <egg><project><name> use the syntax egg/project/name.
Into node remote , patch and step NN there are many nodes in function of the project request.

Every recipes must be saved in a file named conf.egg and store into a folder with the same name of the field egg/project/name. So a complete build system must be a collection of folders into a single main folder. This main folder I named ‘repo’ from repository. Ad example the folder rpi2_repo, a very simple project, have the following tree files
.
├── busybox
│   ├── busybox_defconfig_arm
│   ├── busybox_init
│   └── conf.egg
├── conf.egg
├── linux
│   └── conf.egg
└── uboot
    └── conf.egg

the conf.egg file on main folder rpi2_repo is a special file : it describe the configuration file for all recipes into repo. Ad ex for this repo the file contain:

<?xml version="1.0"?>
<egg>
  <conf>
-----
  </conf>
  <defaults>
    <step id="0">
      ….
    </step>
    <step id="1">
      ...
    </step>
  </defaults>
</egg>

Both the files recipes as the main configuration file is organizzed by step or level so a same recipes can build a different out because at every step can configure the contour: the compile, the option or the architetture. In this mode is very fast the reuse of the recipes.

Recipes description:

NODE: name
FIELD	OPT	DESCRIPTION
egg/project/name	no	Insert the project name .Must be the name of the folder where is this conf.egg file

NODE: remote
FIELD	OPT	DESCRIPTION
egg/project/remote/method	no	Available method: / wget / git / svn / apt / file(rsync)
egg/project/remote/url	no	Url to file to download , (with no filename...)
egg/project/remote/file	no	Url to file to download , (only filename )
egg/project/remote/key/url	yes	Url to sign file to download , (with no filename…)
egg/project/remote/key/file	yes	Url to sign file to download , (only filename )
egg/project/remote/branch	yes	In case of git method can insert branch to download
egg/project/remote/revision	yes	In case of svn method can insert revison to download

Examples of remote node :

    <name>linux</name>
    <remote>
      <method>git</method>
      <url>https://github.com/raspberrypi</url>
      <file>linux.git </file>
      <branch>rpi-4.12.y</branch>
    </remote>

    <remote>
      <method>wget</method>
      <url>https://cdn.kernel.org/pub/linux/kernel/v4.x</url>
      <file>linux-4.10.9.tar.xz</file>
      <key>
        <url>https://cdn.kernel.org/pub/linux/kernel/v4.x</url>
        <file>linux-4.10.9.tar.sign</file>
      </key>
    </remote>

NODE: patch id=N example <patch id=”0”>
FIELD	OPT	DESCRIPTION
egg/project/patch/method	no	Available method: / wget / git / svn / apt / file(rsync)
egg/project/patch/url	no	Url to file to download , (with no filename...)
egg/project/patch/file	no	Url to file to download , (only filename )
egg/project/patch/key/url	yes	Url to sign file to download , (with no filename…)
egg/project/patch/key/file	yes	Url to sign file to download , (only filename )
egg/project/patch/branch	yes	In case of git method can insert branch to download
egg/project/patch/revision	yes	In case of svn method can insert revison to download
egg/project/patch/dir	yes	In case of directory of source patches, set here
egg/project/patch/dest_dir	yes	In the specified patch will be apply to a source project subdir
egg/project/patch/apply id=N	yes	In case of dir is defined , you can inform the system what file can applied

Examples of patch node :

    <patch id=”0”>
      <method>file</method>
      <url>$REPO/mypatch</url>
      <file>0001-patch-version.patch </file>
    </patch>
    <patch id=”1”>
      <method>file</method>
      <url>$REPO/mypatch</url>
      <file>0002-patch-config.patch </file>
    </patch>

NODE : build
FIELD	OPT	DESCRIPTION
egg/project/build/step id=N	no	Define the step N of build . Every step have associated a spicified configuration in main conf.egg file of the repo
egg/project/build/silent	no	Can define verbose build with ‘no’ or mute build ‘yes’
egg/project/build/thread	no	Define max thread num to make (-jN)
egg/project/build/path	yes	Define an action to current $PATH variable. In this can define action before the build action and after the build action. / Insert pre node to add an action before the build action for this step and insert the post node to add an action after the build action .
egg/project/build/path/pre	yes	Change the $PATH before build action
egg/project/build/path/post	yes	Change the $PATH after build action
egg/project/build/path/pre/set	yes	Set the $PATH in function of the value inserted in this node before the build step
egg/project/build/path/pre/add id = N	yes	Add to current $PATH the value inserted in this node, can insert more node in sequence order with the id field , before the build step
egg/project/build/path/pre/remove id = N	yes	Remove from the current $PATH the value inserted in this node, can insert more node in sequence order with the id field , before the build step
egg/project/build/path/post/set		Set the $PATH in function of the value inserted in this node after the build step
egg/project/build/path/post/add id = N		Add to current $PATH the value inserted in this node, can insert more node in sequence order with the id field , after the build step
egg/project/build/path/post/remove id = N		Remove from the current $PATH the value inserted in this node, can insert more node in sequence order with the id field , after the build step

Example path pre/post

<path>
   <pre>
      <set >$USER_PATH</set>
<add id=”0”>$DEPLOY/bin</add>
   </pre>
   <post>
<remove id=”0”>$DEPLOY/bin</add>
   </post>
</path>

egg/project/build/configure	yes	Define the configure step : can be optional if configure , configure.ac , Configure or Makefile.ac isn’t defined in source files.
egg/project/build/configure/pre id = N		As in the previous path node, can define action before after the configure phase. There are three kind of action: code, source, scripts / code: / insert a fragment of bash shell code. Will be executed on configure phase according to the ID(N) step. For any fragment will check the return value an break the execution in case of error. / source / usually used to expand the build system , can source a bash script or var directly into generate configure script. / script / In case of complicated procedure to realized with code mode, is possible to run a bash script
egg/project/build/configure/pre/code		Insert into the generate bash script the code defined here ex: / <code> cp $SOURCE/init $DEPLOY <code>
egg/project/build/configure/pre/source		Insert into the generate bash script the code defined here ex: / <source> /home/some_my_def.sh <source>
egg/project/build/configure/pre/script		Insert into the generate bash script the script defined here ex: / <script> /home/myscrip.sh <script>
egg/project/build/configure/extra id = N		Append to configure call the argument defined here: ex: / <extra id="0">--prefix=$DEPLOY</extra> / <extra id="1">--target=$CROSS</extra>
egg/project/build/configure/post id = N		As in the previous path node, can define action after the configure phase. There are three kind of action: code, source, scripts / code: / insert a fragment of bash shell code. Will be executed on configure phase according to the ID(N) step. For any fragment will check the return value an break the execution in case of error. / source / usually used to expand the build system , can source a bash script or var directly into generate configure script. / script / In case of complicated procedure to realized with code mode, is possible to run a bash script
egg/project/build/configure/post/code		Insert into the generate bash script the code defined here ex: / <code> cp $SOURCE/init $DEPLOY <code>
egg/project/build/configure/post/source		Insert into the generate bash script the code defined here ex: / <source> /home/some_my_def.sh <source>
egg/project/build/configure/post/script		Insert into the generate bash script the script defined here ex: / <script> /home/myscrip.sh <script>

NOTE about pre/post action:

With the xml is possible to insert more command into a single node. Is important to note with in this case only last command is checked . Can Try to generate output script and see the difference. Furthermore , the pre/post action have the sequence id to a hard order to execute the bash shell command. In case have inserted more line in a single node can change the execute order . About the ‘>’ , ‘>>’, ‘<’ , ‘<<’ will translated from xmlstartlet with final errors. Partially can use tee : example : echo “rosa” | tee out

example of configure node (from a gcc recipe):

<configure>
   <pre id="0">
      <code>rm -rf $SOURCE/gmp</code>
   </pre>
   <pre id="1">
      <code>rm -rf $SOURCE/mpc</code>
   </pre>
   <pre id="2">
      <code>rm -rf $SOURCE/mpfr</code>
   </pre>
   <pre id="3">
      <code>rm -rf $SOURCE/isl</code>
    </pre>
    <pre id="4">
     <code>rm -rf $SOURCE/cloog</code>
    </pre>
    <pre id="5">
     <code>A=$(ls -d $SOURCES/gmp/*);ln -s $A $SOURCE/gmp</code>
    </pre>
    <pre id="6">
     <code>A=$(ls -d $SOURCES/mpc/*);ln -s $A $SOURCE/mpc</code>
    </pre>
    <pre id="7">
     <code>A=$(ls -d $SOURCES/mpfr/*);ln -s $A $SOURCE/mpfr</code>
    </pre>
    <pre id="8">
     <code>A=$(ls -d $SOURCES/isl/*); ln -s $A $SOURCE/isl</code>
    </pre>
    <pre id="9">
     <code>A=$(ls -d $SOURCES/cloog/*);ln -s $A $SOURCE/cloog</code>
    </pre>
       <extra id="0">--target=$CROSS</extra>
       <extra id="1">--prefix=$DEPLOY</extra>
       <extra id="2">--enable-shared</extra>
       <extra id="3">--enable-threads=posix</extra>
       <extra id="4">--enable-__cxa_atexit</extra>
       <extra id="5">--enable-clocale=gnu</extra>
       <extra id="6">--enable-languages=c,c++</extra>
       <extra id="7">--disable-multilib</extra>
</configure>

egg/project/build/make id = N	no	Define a build procedure . In a single step can be more than a one make node. In case of project A depend from B with B depend from A project is easy cut the build process in pieces to jump from projects. For this reason is important the fields pri (build priority )
egg/project/build/make/priority	no	Define the build priority for the rules defined into this make node. Low number have high priority (0= max priority). The build system sort the priority for priority build sequence. Into a single step can build more than once the same project if in recipes are present different make nodes.
egg/project/build/make/thread	No	Is the max number of parallel thrad to execute make ( -j param )
egg/project/build/make/rule id = N	no	Call a rule in makefile. To define what rule see name node
egg/project/build/make/rule/name	no	Define the rule to call with make : Make all <rule><name>all</name></rule>
egg/project/build/make/rule/thread	yes	If specified set the max number of parallel thread. Ex <thread>1</thread> / If not specified the max number thread is as specified in egg/project/build/make/thread
egg/project/build/make/rule/pre id = N		As in the previous configure node, can define action before after the make rule phase. There are three kind of action: code, source, scripts / code: / insert a fragment of bash shell code. Will be executed on configure phase according to the ID(N) step. For any fragment will check the return value an break the execution in case of error. / source / usually used to expand the build system , can source a bash script or var directly into generate configure script. / script / In case of complicated procedure to realized with code mode, is possible to run a bash script
egg/project/build/make/rule/pre/code		Insert into the generate bash script the code defined here ex: / <code> cp $SOURCE/init $DEPLOY <code>
egg/project/build/make/rule/pre/source		Insert into the generate bash script the code defined here ex: / <source> /home/some_my_def.sh <source>
egg/project/build/make/rule/pre/script		Insert into the generate bash script the script defined here ex: / <script> /home/myscrip.sh <script>
egg/project/build/make/rule/post id = N		As in the previous configure node, can define action after the make rule phase. There are three kind of action: code, source, scripts / code: / insert a fragment of bash shell code. Will be executed on configure phase according to the ID(N) step. For any fragment will check the return value an break the execution in case of error. / source / usually used to expand the build system , can source a bash script or var directly into generate configure script. / script / In case of complicated procedure to realized with code mode, is possible to run a bash script
egg/project/build/make/rule/post/code		Insert into the generate bash script the code defined here ex: / <code> cp $SOURCE/init $DEPLOY <code>
egg/project/build/make/rule/post/source		Insert into the generate bash script the code defined here ex: / <source> /home/some_my_def.sh <source>
egg/project/build/make/rule/post/script		Insert into the generate bash script the script defined here ex: / <script> /home/myscrip.sh <script>

Example of make node (gcc recipe step 3)

<make id="0">
   <priority>10</priority>
       <rule id="0">
        <name>all-gcc</name>
       </rule>
       <rule id="1">
        <name>install-gcc</name>
        <thread>1</thread>
        <post id="0">
        <code>$CROSS-gcc -v</code>
        </post>
       </rule>
</make>
<make id="1">
   <priority>20</priority>
       <rule id="0">
        <name>all-target-libgcc</name>
       </rule>
       <rule id="1">
        <name>install-target-libgcc</name>
        <thread>1</thread>
       </rule>
</make>
<make id="2">
   <priority>30</priority>
      <rule id="0">
        <pre id="0">
        <code>rm $DEPLOY/$CROSS/lib/libc.so ; echo 'GROUP ( libc.so.6 libc_nonshared.a )' | tee $DEPLOY/$CROSS/lib/libc.so
</code>
        </pre>
        <name>all</name>
      </rule>
      <rule id="1">
        <name>install</name>
        <thread>1</thread>
      </rule>
</make>

In this example make id 0,1,2 have priority 10,20,30 . In this case build at priority 10 gcc then build at priority 15 glibc , then next build to gcc at priority 20 and then build yet glibc at priority 25 an finally build gcc at priority 30.

CONFIGURATION FILE

 As defined in previous paragraph, a repo is a collection of folder with a conf.egg file : this is the main configuration file. The structure of this xml file Is as described here.

NODE: conf
FIELD	OPT	DESCRIPTION
egg/conf	no	Describe the main configuration , common for all step of system variable s. This variables are exported on build variable of all projects
egg/root	no	Define the exported variable $ROOT. Is the main folder with contain all generate / clone d file from current repo
egg/repo	no	Define the exported variable $ROOT. Is the folder where is copied the current repo
egg/sources	no	Define the exported variable $SOURCES. / Is the folder where is expanded / cloned the source of any project
egg/store	no	Define the exported variable $STORE. / Is the folder where is stored all source tar file. Note : if also the source is downloaded from git/svn/file method a tarball is always created and will be update if needed.
egg/images	no	Define the exported variable $IMAGES. / IS the folder where is created the output image
egg/build	no	Define the exported variable $BUILD. / Is the folder where are created all script build and , for each project, the project build folder.
egg/editor	no	Define the exported variable $EDITOR. / Is the program to user as file editor
egg/path	no	Define the exported variable $PATH. / IS the initial value for $PATH
egg/ld_library_path	no	Define the exported variable $LD_LIBRARY_PATH.
egg/user_env id = N	No	Whit this node can define new global user variable. A variable create in this mode is global and exported in all script generated

Example of conf node:

<conf>
    <root>$HOME/ebuild</root>
    <repo>$ROOT/repo</repo>
    <sources>$ROOT/sources</sources>
    <store>$ROOT/store</store>
    <images>$ROOT/images</images>
    <build>$ROOT/build</build>
    <editor>vim</editor>
    <path>$USER_PATH</path>
    <ld_library_path>$USER_LIB_PATH</ld_library_path>
    <user_env id="0">
      <name>USER_PATH</name>
<value>
$ROOT/images/x86_64_sysroot/bin:	$ROOT/images/x86_64_sysroot/x86_64-pc-linux-gnu/bin
</value>
    </user_env>
    <user_env id="1">
      <name>USER_LIB_PATH</name>
      <value>
$ROOT/images/x86_64_sysroot/lib64:
$ROOT/images/x86_64_sysroot/lib
</value>
    </user_env>
</conf>

Node : step id = N
FIELD	OPT	DESCRIPTION
egg/defaults/step	no	Define a level/ step of build
egg/defaults/step/step_name	no	Define the name of the create folder in $IMAGES. In this folder where is the build output
egg/defaults/step/info	no	In this fields can insert a brief description of this step build
egg/defaults/step/cc	no	The value in this field is exported in $CC global variable
egg/defaults/step/cxx	no	The value in this field is exported in $CXX global variable
egg/defaults/step/as	no	The value in this field is exported in $AS global variable
egg/defaults/step/ld	no	The value in this field is exported in $LD global variable
egg/defaults/step/nm	no	The value in this field is exported in $NM global variable
egg/defaults/step/ar	no	The value in this field is exported in $AR global variable
egg/defaults/step/strip	no	The value in this field is exported in $STRIP global variable
egg/defaults/step/cflags	no	The value in this field is exported in $CFLAGS global variable
egg/defaults/step/cppflags	no	The value in this field is exported in $CPPFLAGS global variable
egg/defaults/step/cxxflags	no	The value in this field is exported in $CXXFLAGS global variable
egg/defaults/step/ldflags	no	The value in this field is exported in $LDFLAGS global variable
egg/defaults/step/libs	no	The value in this field is exported in $LIBS global variable
egg/defaults/step/cpath	no	The value in this field is exported in $CPATH global variable
egg/defaults/step/c_include_path	no	The value in this field is exported in $C_INCLUDE_PATH global variable
egg/defaults/step/cplus_include_path	no	The value in this field is exported in $CPLUS_INCLUDE_PATH global variable
egg/defaults/step/arch	no	The value in this field is exported in $ARCH global variable
egg/defaults/step/cross	no	The value in this field is exported in $CROSS global variable
egg/defaults/step/cross_compile	no	The value in this field is exported in $CROSS_COMPILE global variable

Example of step node

<defaults>
    <step id="0">
      <step_name>rpi2_image</step_name>
      <info>build uboot from rpi2</info>
      <cc>gcc</cc>
      <cxx>g++</cxx>
      <as>as</as>
      <ld>ld</ld>
      <nm>nm</nm>
      <ar>ar</ar>
      <strip>strip</strip>
      <asflags>
-mfpu=neon-vfpv4 -march=armv7ve
</asflags>
      <cflags>
-O3 -mfpu=neon-vfpv4 -march=armv7ve -mtune=cortex-a7
</cflags>
      <cppflags>
-O3 -mfpu=neon-vfpv4 -march=armv7ve -mtune=cortex-a7
</cppflags>
      <cxxflags>
-O3 -mfpu=neon-vfpv4 -march=armv7ve -mtune=cortex-a7
</cxxflags>
      <ldflags></ldflags>
      <libs></libs>
      <cpath>
$ROOT/images/sysroot_x86_64/arm-none-eabi/include
</cpath>
      <c_include_path></c_include_path>
      <cplus_include_path/></cplus_include_path>
      <arch>arm</arch>
      <cross>x86_64</cross>
      <cross_compile>arm-none-eabi-</cross_compile>
    </step>
<defaults>

Note : there also the following global variable defined from host system:
- $HW_ARCH : the host system architetture ex: x86_64
- $NATIVE : the current host system linux ex : x86_64-linux-gnu
- $DEPLOY : is $IMAGES/$STEP_NAME

COMMANDS

 the scripts egg have more commands and subcommands and option. This command are described here.

Note : case sensitive
Command	Description
help	Aid for command syntax
cat	Print the content of <project>/conf.egg
source	Generate download script and download source
gen	Generate build script
do	Start all build step/projects (configure & build)
build	Start all build step/projects (only build)
redoall	Restart all build cycle : source+gen+do
cd	Open a work shell of project <projecegg > -B source_download source 0t>
distclean	Remove all builds for all step/projects
edit	Edit a project/conf.egg file
reset	Remove all file downloaded / generated
info	Show program info
pack	Pack the output to a tar.bz2
multi	Sequence building of repos
list	List current repo
setrepo	Set current repo from input <new repo>
freeze	Set the status of project as stable ( builded ok)
hot	Set the status of project as ‘to configure’
clone	Clone a specified project/conf.egg to <new project>
pri	Mode, set, swap make node priority

‘egg’ request in the same directory of the script a link named repo to the real folder of repository. This is the current repo or repo in use. The command setrepo can rewrite this link or an user can set manually this , before launch the ‘egg’ script. If the repo is invalid the script do not work and exit with error. If setrepo work ok will list the current repo. For ex.

finsoft@finsoft-720:~/eggX$ ln -s x86_64_sysroot_repo/ repo
finsoft@finsoft-720:~/eggX$ ./egg
 Copyright (C) 2017 Angelo Coppi. <angelogkcop@hotmail.com>
 This is free software; see the LICENSE file for copying conditions.
 There is NO warranty; not even for MERCHANTABILITY or FITNESS
 FOR A PARTICULAR PURPOSE.
 Current repo : x86_64_sysroot_repo/
 quit/exit for exit iterative mode
 egg > setrepo
 Copyright (C) 2017 Angelo Coppi. <angelogkcop@hotmail.com>
 This is free software; see the LICENSE file for copying conditions.
 There is NO warranty; not even for MERCHANTABILITY or FITNESS
 FOR A PARTICULAR PURPOSE.
 -------------------- -------------------- --------------------
 WARNING : - No repo set
 > - Please select one from the following repository
 -------------------- -------------------- --------------------
 1) - arm-linux-tools-repo
 2) - arm-none-tools-repo
 3) - LFS_repo
 4) - rpi2_repo
 5) - sysroot_repo
 6) - x86_64_sysroot_repo
4
 -------------------- -------------------- --------------------
 REPO /home/finsoft/eggX/repo /home/finsoft/eggX/rpi2_repo
 -------------------- -------------------- --------------------
 STEP : 0 1 - to configure uboot_0
 -------------------- -------------------- --------------------
 STEP : 1 2 - to configure linux_1
 -------------------- -------------------- --------------------
 STEP : 1 3 - to configure busybox_1
 -------------------- -------------------- --------------------
 STATUS to configure rpi2_image
  -- 3 sec

If the repository is valid is possible to generate the image. The most fast command is redoall , but with this command discard all previous work, and for large project this is not a good idea. For the example repo have two levels : step 0 and step 1. Step 0 is used for build uboot , step 1 for build linux kernel and busybox. Step 0 is configured for build with arm compiler arm-none-eabi , step 1 is configured to build with arm-linux-gnueabi,these toolkit are generated from sysroot_repo and x86-64_toolkit_repo. ( you can see rpi2_repo/conf.egg ).
If do the command source 0/1 ‘egg’ script execute many step :

1. On $BUILD path is created build directory : one for every pair project_name-step , so in the example case is created uboot_0, linux_1, busybox_1 folder
2. Generate bash download script for all project in repository in the build folder: download.sh
3. execute in priority order the download of source in mode as described in remote node of conf.egg project file. For any downloaded project the tar file is store in the $STORE folder. If the method used for download the file is git/svn/file or apt a backup tar file is created and stored in $STORE path. In this mode is created a backup copy of all source packet , and is possible to work also off line. For every file downloaded the script try to download also the sign file associated. It try to download the file <filename>.sig , .sign, .asc, .md5 .sha1. If a sign is found so gpg/md5sum/sha1sum is called and the sign is checked. ( note key sign must be imported in gpg before this step). In all case a sign file md5 is generated to quickly check the tar file. All this step are logged in the screen. If download fail the script can try 5 once to download the file. Also if sign fail the script car retry to download the file, but if sign file is missing the file is assumen ‘good’ and the md5sum is generated.
4. Generate bash patch script for all project in repository in the build folder: patch.sh
5. execute in priority order / patch id sequence the download of all defined path as described in patch node in project/conf.egg. As in source download step also the patch file is stored in $STORE folder with a md5sum file.
6. Apply all patches downloaded in priority order / patch id.

For example the source 0 produce the following output

egg > source 0
 Copyright (C) 2017 Angelo Coppi. <angelogkcop@hotmail.com>
 This is free software; see the LICENSE file for copying conditions.
 There is NO warranty; not even for MERCHANTABILITY or FITNESS
 FOR A PARTICULAR PURPOSE.
 -------------------- -------------------- --------------------
 CONF : uboot 0 download source
 -------------------- -------------------- --------------------
 DWLOAD: 0 uboot_0 rpi2_image
    - Git source uboot
Da git://git.denx.de/u-boot
 * branch master -> FETCH_HEAD
 -------------------- -------------------- --------------------
 -------------------- -------------------- --------------------
 CONF : uboot 0 patch source
 -------------------- -------------------- --------------------
 PATCH: 0 uboot_0 rpi2_image
 -------------------- -------------------- --------------------
  -- 59 sec
 egg >

after this command the $BUILD folder contain :

finsoft@finsoft-720:~/ebuild/build$ tree rpi2_image/
rpi2_image/
└── uboot_0
    ├── download.sh
    ├── patch.sh
    └── status

and the $SOURCE folder contain:

finsoft@finsoft-720:~/ebuild/sources$ tree -L 2
.
└── uboot
    ├── api
    ├── arch
    ├── board
    ├── cmd
    ├── common
    ├── config.mk
    ├── configs
    ├── disk
    ├── doc
    ├── drivers
    ├── dts
    ├── examples
    ├── fs
    ├── include
    ├── Kbuild
    ├── Kconfig
    ├── lib
    ├── Licenses
    ├── MAINTAINERS
    ├── Makefile
    ├── net
    ├── post
    ├── README
    ├── scripts
    ├── snapshot.commit
    ├── test
    └── tools

Now we can prepare to build uboot project, do the command gen 0

 egg > gen 0
 Copyright (C) 2017 Angelo Coppi. <angelogkcop@hotmail.com>
 This is free software; see the LICENSE file for copying conditions.
 There is NO warranty; not even for MERCHANTABILITY or FITNESS
 FOR A PARTICULAR PURPOSE.
 -------------------- -------------------- --------------------
 STEP : 0 PRI : 1 uboot created done !
 -------------------- -------------------- --------------------
  -- 2
Are generate the build scripts. The build folder contain:
.
├── step_0.sh
└── uboot_0
    ├── bootstrap.sh
    ├── build -> /home/finsoft/ebuild/sources/uboot
    ├── build_1.sh
    ├── clean.sh
    ├── distclean.sh
    ├── download.sh
    ├── patch.sh
    ├── rebuild.sh
    ├── setenv.sh
    └── status

Note: Uboot not is a autoconf project so build folder is the same of source folder . ‘egg’ monitoring this condition and generate this link. In detail:

1. bootstrap.sh : script to call configure in this case no do nothing because configure is missing
2. build_1.sh : script to call make def config, all install etc
3. setenv.sh : script to set the build environment. Usually for manual build have to do source setenv.sh
4. clean.sh,distclean.sh,rebuild.sh : same action in the name…

Now we can build the uboot project, do ‘do 0’ command. The output is the following

egg > do 0
 Copyright (C) 2017 Angelo Coppi. <angelogkcop@hotmail.com>
 This is free software; see the LICENSE file for copying conditions.
 There is NO warranty; not even for MERCHANTABILITY or FITNESS
 FOR A PARTICULAR PURPOSE.
 -------------------- -------------------- --------------------
 BUILD : 1 uboot_0 rpi2_image
        ... done 0 sec
        Make rpi_2_defconfig-8:8 start
        ... done 4 sec
        Make DEVICE_TREE=bHow it workscm2836-rpi-2-b all-8:8 start
        ... done 16 sec
 -------------------- -------------------- --------------------
  -- 20 sec

the build phase call make rpi_2_defconfig with 8 on 8 thread active ( -j8 )and make DEVICE_TREE=bcm2836-rpi-2-b all also with -j8. Note do not call install because this rule isn’t in Makefile. This is suplied in uboot recipe with rule/post/action:
<post id="0">
   <code>
mkdir -p $DEPLOY/boot;
install $BUILD/u-boot.bin $BUILD/u-boot-*.bin $DEPLOY/boot;
   </code>
</post>

so the image folder in accordance have the following structure:
finsoft@finsoft-720:~/ebuild/images/rpi2_image$ tree -L 2
.
└── boot
    ├── u-boot.bin
    ├── u-boot-dtb.bin
    └── u-boot-nodtb.bin

In the same mode we can do source 1 and gen 1 and do 1.
Or can insert redoall . Redoall execute in automatic mode the command source 0, gen 0, do 0,source 1 , gen 1 , do 1.

for a more detailed description of a specific command can try to do help <command> ex.

egg > help edit
 Copyright (C) 2017 Angelo Coppi. <angelogkcop@hotmail.com>
 This is free software; see the LICENSE file for copying conditions.
 There is NO warranty; not even for MERCHANTABILITY or FITNESS
 FOR A PARTICULAR PURPOSE.
 -------------------- -------------------- --------------------
 HELP : command : edit
      > $1 : name : request
      > if name = self edit this script
      > if name = self.conf edit current repo/conf.egg
      > if name = a name of a project in repo edit repo/name/conf.egg
      > if name = self.repo edit one by one all repo's conf.egg files
      > if name = --format format all conf.egg xml files
      > ex : ./egg edit binutils
      > the edit is defined in repo/conf.egg/<editor> fields, ex vim
 -------------------- -------------------- --------------------
  -- 1 sec

OPTIONS

‘egg’ is a bash script so can think is easy the debug … not exactly!
I have added in the script some feature to help in debug phase.

There are the following options:
- -D or --debug
- +W or --warning
- -B or --break
- -X or --deepbreak
- -S or --step
- -T or --test

-D or –debug : simple execute set -x and trace the script
+W or --warning : more verbose operation
-B or –break : set a breakpoint at specific function and break the execution , set on trace , set on step by step and print the argument passed as input at the function. The calling function into this function are executed with trace on but, with step by step, off.
-X or –deepbreak : set a breakpoint at specific function and break the execution , set on trace , set on step by step and print the argument passed as input at the function. The called function into this function are executed with trace on and with step by step on. ( step into )
-S or –step : set trace on and step by step from start of script
-T or –test : call a specific function with the parameter passed from input with trace on step by step on

ex.

 egg > -B source_download source 0
 Copyright (C) 2017 Angelo Coppi. <angelogkcop@hotmail.com>
 This is free software; see the LICENSE file for copying conditions.
 There is NO warranty; not even for MERCHANTABILITY or FITNESS
 FOR A PARTICULAR PURPOSE.
 -------------------- -------------------- --------------------
 WARNING : - Set debug breakpoint
 > - At function source_download
 -------------------- -------------------- --------------------
 -------------------- -------------------- --------------------
 ARGV : NUM:1 0
+(./egg:4293): source_download(): trap read debug
++(./egg:4295): source_download(): read